José Carlos Mayoral Baños

Summary Robot Perception Lecture May 12th 2016

- Cameras
  - Continues....
  - General Cameras
    - Matrix P representations:
      - Columns.. represents the vanishing points, in other world the world axis directions.
      - Rows... axis planes (x=0 and y=0) and principle plane.
      - General projective camera (P) maps x = PX
      - Matrix P is rank 3, with just 1D null space.
      - Null space is a 4D vector which shows the camera center at homogeneous coordinates.
      - If the null space is finite then the camera is finite, other wise is a infinite camera.
      - The principal plane for finite centers a 4 vector abcd represents the equation ax+by+cz+d = 0, remembering that points in the principal plane are the ones that are mapped to the infinity.
      - Principal axis is a normal of the principal plane.
      - Matrix P divides itself in blocks M|p4.
      - The last row of M shows the principal axis direction.
      - To find a backprojection from the image poitn to the projective space the pseudoinverse is needed.
      - Having the matrix P and the projective of a point X to x= PX we can compute the depth since PC = 0 being C the center of the camera.
      - w= m3(X-X) where m3 is the direction of the principal axis.
      - Normalizing M and m3 then w is the depth of X from C in the direction of principal axis.
      - SVD can be used to obtain intrinsic and extrinsic parameters.
      - Last column of V s the null space or C.
      - Other way to analyze P is taking M and use QR to find KR where K is the calibration matrix and R represents the homogeneous transformation.
      - K matrix considers skew and focal length.
      - For Real world homographies are euclidean, general are used for generalization.
      - Infinity cameras has a singular M.
      - For calibration, given correspondences are used to calculate P.
      - Restricted camera estimation problem gives correspondences and some knowledge of P.
      - In vision, true projective camera is assumed but it doesn't consider lens distortion.
      - DLT or Gold standard can be used to compute P.
      - Lens distortion is solved considering it as radial.
- Multiple View Geometry.
  - Represent geometric relations between two views of the same plane.
  - Solver 3 problems.
    - Knowing matrix P and x how will be the correspondence point in the other plane.
    - Given both corresponding point, calculates P and P'
    - Give P, P' and both correspondencies, calculate 3D position of the points.
  - If both views are just a translation are called auto-epipolar.
  - Epipolar Geometry.
    - Projective geometry of two views that just depends on the camera's internal parameters and relative poses of the cameras.
    - A matrix F captures the geometry of the epipolar geometry.
    - F computing is similar to homography matrix.
    - With F, P and P' camera properties matrix can be deduced.
    - Baseline connects both camera centers.
    - Epipolar plane is created with the baseline and the correspondence points.
    - Interesection of baseline and image planes are called Epipoles.
    - At rotating points the whole plane rotates according the baseline.
    - Epipolar line is the intersection of an epipolar plane with the image plane.
    - For correspondence points between two image we only need to look for the correspondence along the epipolar line.
    - All epipolar lines intersect at the epipole.